## Slide 1: Requirements writing exercise

## Slide 2: Introduction – exercise context
This exercise introduces basic concepts about requirements writing.
The main objective is to write scooter motor requirements from customer requirements given in this document.
The company MU Scooters Inc. is looking for a supplier of electric motors. You (student) are part of a company that manufactures electric motors.
MU Scooters Inc
You
Customer requirements
Motor requirements

## Slide 3: Introduction – exercise tasks
The exercise will consist of the following tasks:
Read carefully customer requirements given in the following slides. Remember that these requirements may be given in an informal and unstructured way. The objective is to convert what the customer asks for into formal requirements for the motor.
Start writing two motor requirements.
Create a requirement set and requirements in MATLAB Requirement Editor.
Complete the attributes present in the Requirement Editor.
Complete the whole requirement set taking into account the information given by the customer.
Take into account the guidelines given in class theory. The exercise will be evaluated following those guidelines.
The deliverable will contain a MALTAB requirements set file (slreqx) and a word file imported directly from the editor.

## Slide 4: Electric motor customer requirements
1

## Slide 5: General description of the scooter
In-wheel motor
Embedded battery and electronics
Aluminium frame
Display
Manual throttle
Maximum scooter speed: 25 km/h

## Slide 6: Typical operation profiles
Profile 1
Profile equivalent torque: 1.27 Nm
Maximum traction torque: 2.92 Nm
Maximum braking torque: 6.09 Nm
Maximum speed: 1503 rpm

## Slide 7: Typical operation profiles
Profile 1

## Slide 8: Typical operation profiles
Profile 2
Profile equivalent torque: 1.79 Nm
Maximum traction torque: 7.76 Nm
Maximum braking torque: 5.88 Nm
Maximum speed: 2649 rpm

## Slide 9: Typical operation profiles
Profile 2

## Slide 10: Typical operation profiles
Profile 3
Profile equivalent torque: 1.03 Nm
Maximum traction torque: 7.20 Nm
Maximum braking torque: 5.84 Nm
Maximum speed: 3320 rpm

## Slide 11: Typical operation profiles
Profile 3

## Slide 12: Other requirements
24 V battery voltage.
In-Wheel motor.
10-inch, inflatable.
Maximum weight: 4 kg

## Slide 13
Eskerrik asko
Muchas gracias
Thank you
Jon del Olmo Larrañaga
jdelolmo@mondragon.edu
Iosu Aizpuru Larrañaga
iaizpuru@mondragon.edu
Orona Ideo - Fundazioa eraikuntza
Jauregi Bailara, z.g.
20120 Hernani (Gipuzkoa)
Tel. : +(34) 943 739765
www.mondragon.edu