## Slide 1: Scooter motor requirements

## Slide 2: Introduction
This document presents the requirements for a electric scooter motor.

## Slide 3: General description of the scooter
In-wheel motor
Embedded battery and electronics
Aluminium frame
Display
Manual throttle
Maximum scooter speed: 25 km/h

## Slide 4: Typical operation profiles
Profile 1
Profile equivalent torque: 1.27 Nm
Maximum traction torque: 2.92 Nm
Maximum braking torque: 6.09 Nm
Maximum speed: 1503 rpm

## Slide 5: Typical operation profiles
Profile 1

## Slide 6: Typical operation profiles
Profile 2
Profile equivalent torque: 1.79 Nm
Maximum traction torque: 7.76 Nm
Maximum braking torque: 5.88 Nm
Maximum speed: 2649 rpm

## Slide 7: Typical operation profiles
Profile 2

## Slide 8: Typical operation profiles
Profile 3
Profile equivalent torque: 1.03 Nm
Maximum traction torque: 7.20 Nm
Maximum braking torque: 5.84 Nm
Maximum speed: 3320 rpm

## Slide 9: Typical operation profiles
Profile 3

## Slide 10: Other requirements
24 V battery voltage.
In-Wheel motor.
10-inch, inflatable.
Maximum weight: 4 kg

## Slide 11
Eskerrik asko
Muchas gracias
Thank you
Jon del Olmo Larrañaga
jdelolmo@mondragon.edu
Iosu Aizpuru Larrañaga
iaizpuru@mondragon.edu
Orona Ideo - Fundazioa eraikuntza
Jauregi Bailara, z.g.
20120 Hernani (Gipuzkoa)
Tel. : +(34) 943 739765
www.mondragon.edu