## Slide 1: Writing requirements
TESTING AND
VALIDATION
PLATFORMS

## Slide 2: Contents
Properties of requirements
Language of requirements

## Slide 3: Properties of requirements
1

## Slide 4: Requirement examples
Let’s see some requirements and discuss what do you understand:
Response time should be less than 2 seconds.
The system may perform at the maximum rating at all times, except when battery SoC is below 20 %, when it should provide 75 % of the maximum rating.
The converter must minimize losses.
The input range of an analogue input needs to have a maximum voltage of 5 V.

## Slide 5: Common mistakes
When writing requirements, some mistakes are very common:
Very long sentences, requirements look like a novel.
One paragraphs contains more than one requirement. Avoid using conjunctions (and, or, but…).
Avoid subjective words like big, small, minimize, flexible maximize, user-friendly, easy, sufficient, adequate, quick…
Avoid writing conditionals: if it is necessary, in case of,…
Avoid writing implementation (HOW) and write requirements (WHAT).
If you are used to design and implement things, you will tend to write HOW things should be done.

## Slide 6: Common mistakes
When writing requirements, some mistakes are very common:
Very demanding requirements:
  Write numbers but also tolerances. The maximum voltage shall be 10 V ± 2 %.
Example
Some of the major horror stories of the aerospace industry deal with overly-stringent requirements. One contractor was severely criticized for charging $25,000 per coffee pot in airplanes built for the government. But the requirements for the coffee pot were so stringent, that the plane could have crashed and yet no coffee could spill. It cost a great deal to develop the coffee pot and to verify that it met its requirements.

## Slide 7: Characteristics
Requriments characteristics
Feasible
Verifiable
Unambigous
Clear
Complete
Atomic
Legal
Abstract
Technically possible (cost and schedule).
Each statement can be tested. There is a feasible procedure to do so.
Each statement is precise, there are no ambiguities. There is only one interpretation.
Each statement can be understood. There are not spelling or other kind of mistakes.
The requirement defines a single traceable element.
Does not make you break any law.
The requirement does not specify a certain solution. It may be difficult in projects where a solution was already developed.
It contains all the information to understand it.

## Slide 8: Feasible
Technically possible (cost and schedule)
The implementation of a requirement must be finite and cost-effective.
The system shall give full power at any speed.
The system shall give full power up to 2000 rpm.

## Slide 9: Verifiable
Each statement can be tested. There is a feasible procedure to do so.
The process with which a person or machine can check that the system product meets the requirement must be finite and cost-effective.
The output of the program shall usually be given within 10 s.
The output of the program shall be given within 20 s of event X, 60% of the time; and shall be given within 30 s of event X, 100% of the time.
This statement can be verified because it uses concrete terms and measurable quantities.

## Slide 10: Unambiguous
Each statement is precise, there are no ambiguities. There is only one interpretation.
The converter must minimize losses
When the converter is working at its output nominal power, the power losses shall be smaller or equal to a 5 % of the nominal output power.

## Slide 11: Clear
Each statement can be understood. There are not spelling or other kind of mistakes.
The range of an analogue port needs to have a maximum tension of 5 A
The voltage range of all analogue input channels shall be between 0 V and 5 V.

## Slide 12: Atomic
The requirement defines a single traceable element.
The smallest piece of information you can give that on its own is verifiable and complete.
The maximum ratings for analogue input channels shall be 5 V and 200 mA.
The maximum input voltage for analogue input channels shall be 5 V.
The maximum input current for analogue input channels shall be 200 mA.

## Slide 13: Abstract
The requirement does not specify a certain solution. It may difficult in projects where a solution was already developed.
Since we are engineers, we may already have built something like what requirements are asking for.
Even if we known HOW to do it, write WHAT it should do.
An amplifier stage shall amplify the input voltage by a factor of 2.
The input voltage shall be amplified by a factor of 2.

## Slide 14: Complete
It contains all the information to understand it. It has all the characteristics mentioned before.
Inclusion of all significant requirements, whether relating to functionality, performance, design constraints, attributes or external interfaces
The BMS shall indicate the SoC of the battery.
The Battery Management System shall indicate the state of charge of the battery numerically, with maximum jumps of 5%.

## Slide 15: Language of requirements
2

## Slide 16: The language of requirements
There are some standards that help us using the correct language.
We will take the IEEE Standards Style Manual as a reference.
There are some key words that appear in requirements but are not the same:
  Shall
  Should
  May
  Must
  Can

## Slide 17: The language of requirements
Word | Description
shall | indicates mandatory requirements strictly to be followed in order to conform to the standard and from which no deviation is permitted (shall equals is required to).
should | indicates that among several possibilities, one is recommended as particularly suitable without mentioning or excluding others; or that a certain course of action is preferred but not necessarily required (should equals is recommended that).
may | The word may is used to indicate a course of action permissible within the limits of the standard (may equals is permitted to).
Can | can is used for statements of possibility and capability, whether material, physical, or causal (can equals is able to).

## Slide 18: The language of requirements
The Battery Management System shall indicate the state of charge of the battery numerically, with maximum jumps of 5%.
El sistema de gestión de baterías indicará numéricamente el estado de carga de la batería, con saltos máximos del 5 %.
Bateriak kudeatzeko sistemak zenbakiz adieraziko du bateriaren karga-egoera, %5eko gehienezko jauziekin.

## Slide 19: Typical requirements structures
Capability requirement
The stakeholder type shall be able to capability
The operator shall be able to switch off the machine
Capability requirement with constraints
The stakeholder type shall be able to capability
within performance of event
while operational condition.
The operator shall be able to switch off the machine within 3 seconds of overcurrent alarm activation while in rated conditions.

## Slide 20: References
3

## Slide 21: References
Holt, J., Perry, S. A., & Brownsword, M. (2012). Model Based Requirements Engineering (Institution of Engineering and Technology, Ed.).
Hull, E., Jackson, K., & Dick, J. (2011). Requirements Engineering. Springer London. https://doi.org/10.1007/978-1-84996-405-0
IEEE Standards Association. (2021). 2021 IEEE SA Standards Style Manual. https://mentor.ieee.org/myproject/Public/mytools/draft/styleman.pdf

## Slide 22
Eskerrik asko
Muchas gracias
Thank you
Jon del Olmo Larrañaga
jdelolmo@mondragon.edu
Orona Ideo - Fundazioa eraikuntza
Jauregi Bailara, z.g.
20120 Hernani (Gipuzkoa)
Tel. : +(34) 943 739765
www.mondragon.edu